Sequencia
Partner Tools
20 Minute OpenBatch
Review

---
20 Minute Review
20 Minute Review
Suggested use
  - This is intended to show some of the basic functionality of OpenBatch and explain some of the concepts of batch automation
    - It lists the high points of the product
    - It shows some of the typical product screens
  - The first time through run through this slowly,
  - Run through this quickly for a review

---
Batch Automation Elements
Batch Automation Elements
There are three basic elements involved in batch automation
1: Defining the basic processing capability of the equipment
2: Defining recipes for products
3: Making batches
This is all based on the international standard for batch control systems
ISA S88.01 (also known as IEC 61512-01)

---
Batch Automation
Batch Automation
Click here
anytime to return
to this screen
Click here to
go immediately to
Defining
Equipment
Capability
Click here to
go immediately to
Batch
Execution
Click here to
go immediately to
Recipe
Definition

---
Equipment Capability Definitions
Equipment Capability Definitions
The basic capability of the equipment must be defined
  - Capability that is usually product independent
  - Such as; heating, cooling, charging, mixing, transferring, …
  - Associated to specific equipment
- Capability may be performed automatically or manually
- Defined using the Equipment Editor
Equipment
Definition

---
Equipment Editor
Equipment Editor
Define the equipment model using a simple graphical configuration
- The equipment editor is run, off-line, to define what the equipment is capable of doing
- You also use the equipment editor to define the mapping (addresses or names) to the PLC and DCS systems that implement the functions
This defines the configuration that only changes when new processing capability is added, such as new vessels and new piping, or when new control capability is added.

---
Top Level - Process Cells
Top Level - Process Cells
Define a process cell class for each type of process cell being controlled
- Batches run to completion in a process cell
- This follows the S88.01 equipment hierarchy model
  - Process cells
  - Made up of units
  - Units contain equipment phases
- Each OpenBatch server can support multiple process cells
A process cell is (in S88 terms) all of the equipment required to make a batch.
Process cell classes are ways to visually identify different types of cells.

---
Drag and Drop Configuration
Drag and Drop Configuration
Drag and drop a cell class into the workspace to define a cell
- Starting an equipment model is a simple process of creating a process cell class and then creating a specific cell
- Icons represent the process cells, units, and equipment phases
A process cell can contain multiple batches at the same time.

---
Define Units and Flow Paths
Define Units and Flow Paths
This defines a class of units
This defines a specific unit
- Create units the same way
- A unit operates on only one batch at time
- A unit performs major processing actions on a batch
- Define connections between units to show flow paths of materials
This shows connections between units

---
Equipment Phase -
Basic Equipment Capability
Equipment Phase -
Basic Equipment Capability
Equipment phases define what the basic processing equipment is capable of doing
  - Such as heating, mixing, adding ingredients, transferring materials, …
- Each phase is a minor processing action on the batch
- It does not matter if the function is performed manually or automatically
Define a phase and drop it onto the unit definition. This defines an equipment capability available in the unit.

---
Phase Parameters
Phase Parameters
- Phases may have parameters
- Parameters define information to be sent to the phase before it executes
- Examples are
  - temperature setpoints
  - materials to be added
  - amount to be added
  - mixing times
  - heating times
  - ...
The parameter may be used by the controller logic, or referenced in manual instructions
Define the parameters sent to the phase from the recipe

---
Report Parameters
Report Parameters
- Phases may report back values during or after their execution
- Such as
  - Actual amount added
  - Actual temperature
  - Actual pressure
- Report parameters may be manually entered by the operator or automatically collected by control equipment
The reports are sent back by the controller logic, or entered by operators for manual phases
Define the parameters reported back to the recipe from the phase

---
Equipment Interface
Equipment Interface
- The equipment editor is where you specify the interface to the control equipment for the phase
- The interface can be DDE or OPC to PLC or DCS systems
- The interface may be an annotated SOP document for manual operations using Procedure Manager
These are tags in the DCS, or registers in the PLC that the controller logic uses to communicate to OpenBatch
This defines the interface to controller logic.

---
Manual or Automated Functions
Manual or Automated Functions
- Equipment phases may be executed in control equipment, such as DCS or PLC systems
- Equipment phases may be executed manually, where instructions are presented to operators using Sequencia's Procedure Manager
Automated
Phase
Manual
Phase
Step 1: Check vessel
Step 2: Open the drain valve
...
Identify document
that specifies how
to accomplish
the function
Identifies the data exchanged with a section of code in the controller that implements
the function

---
A Full Equipment Model
A Full Equipment Model
Summary
  - OpenBatch's Equipment Editor is used to define the process cells, units, and equipment phases available for batch manufacturing
  - The equipment model is used when creating recipes and when creating batches
  - Click again to see a complete process cell definition
UNIT
Premix B
UNIT
Precharge B
UNIT
Storage B
UNIT
Premix A
UNIT
Precharge D
UNIT
Reactor
UNIT
Storage A
Process
Cell

---
Recipes
Recipes
- Recipes define how to make products
- Recipes are created using the Recipe Editor
- Recipes are executed in the OpenBatch run time system
- Recipes follow the S88.01 standard
Recipe
Definition

---
Recipes and Equipment
Recipes and Equipment
- Recipes use the equipment information defined in the Equipment Editor
- Recipes define the ordering and sequencing of the equipment phases
- The recipes specify when the
  phases are to run, but the
  equipment phases do all of
  the real work
Equipment
Recipe
I say
when
I define
how

---
Recipe Format
Recipe Format
- Recipes are created, and displayed in a graphical format called SFCs - Sequential Function Charts
- This format allows the easy
  display of sequential steps,
  alternate steps, and
  parallel steps

---
Recipe Editor
Recipe Editor
Recipes are made up of Unit Procedures, Operations, and phases
- The recipe editor is used to create and modify recipes
- Usually there is one recipe per product
- The main part of a recipe is the "PROCEDURE"
  - The ordering of actions required to make the product
- The procedure is structured according to the S88.01 model
The same Unit Procedures and Operations can be used in multiple recipes to speed recipe development

---
Rapid Editing
Rapid Editing
Editing shortcuts make it easy to create and edit recipes
- The recipe editor has features to make recipe creation and editing easy and error free.
- Recipes can be modified at any time and made immediately available for execution.
The shortcuts make sure the recipes are correctly defined.

---
Recipe Editing
Recipe Editing
Recipes use the phases defined in the equipment model
- The lowest level of the procedure is a "Recipe Phase"
- A recipe phase references an equipment phase
  - For a specific piece of equipment
  - Or for a class of equipment
I can only use the phases defined in the equipment editor, but I select the order of execution !

---
Recipes in a Simple Table Format
Recipes in a Simple Table Format
Recipes can be displayed and edited in the graphical view or in the table view.
- Simple recipes require simple display
- So simple recipes can be displayed in a table format for occasional users
The table view is more compact and easier to understand for simple recipes

---
Multiple Views
Multiple Views
It is even possible to see the table and graphical view at the same time.
- You can even show the table view and the graphical SFC view at the same time
- Using the recipe editor, recipes can be created in very short times
- Using the alternate views, recipes can be read and reviewed by people not familiar with OpenBatch
These are easy to understand, but they are also very powerful tools !

---
Phase Parameters
Phase Parameters
Define the parameter values that will be sent to the equipment phase when this recipe runs.
- When you create a recipe you can specify the specific parameters to be sent to a phase before it executes
- Such as a temperature setpoint, or the amount of material to add
This is how I use a phase to perform different tasks based on the recipe I am defining !

---
Recipe Summary
Recipe Summary
With the right authority, recipes can be created and modified at any time.
- Recipes are the key element of batch automation
- They define how to make a specific product, without specifying how the underlying functions are preformed
- OpenBatch includes other information as well
  - Formula values
  - Author identification
  - Comments
  - Equipment requirements
The next time the recipe is used, the new definition is picked up

---
Batch Execution
Batch Execution
- OpenBatch is not just a recipe editor, it also executes the recipes
- There is a run-time component of OpenBatch that runs recipes under operator control
Batch
Execution

---
Recipes and Operations
Recipes and Operations
- Operations is where it all comes together
- Operators execute batches and select equipment they will run against
I will use your equipment definitions
I will use your recipe definitions

---
Batch Execution
Batch Execution
Usually the OpenBatch server is configured to auto start, so I don't have to worry about this software stuff
- Batches are executed in the OpenBatch run time system
- OpenBatch runs as a Windows-NT service
  - OpenBatch can auto start, so no operator intervention is required
- An OpenBatch server can communicate to multiple PLC and DCS systems to control multiple process cells
- OpenBatch uses DDE and OPC to communicate to control equipment
This is sometimes used to aid in startup and commissioning !

---
Operation - Batch List
Operation - Batch List
- The Batch List is usually shown as an Active-X control in an HMI, or in a WEB Browser
- This shows all of the batches currently scheduled, running, and completed in the process cell.
This shows the batches currently in the batch list.
This shows the recipe the batch is running.
This shows when the batch started.
This shows how long the batch has been running.
This shows the state of the batch; idle, running, complete, held, aborted.
This shows what equipment the batch is running in.

---
Operation - Controlling Batches
Operation - Controlling Batches
- A simple right click brings up the menu to add and control batches
- Batches can run in manual, semi-automatic, or automatic mode
- Operators can start, hold, restart, stop, or abort batches
  - If they have the correct privileges
I use the "Create Control Recipe" command to add new batches to the batch list
I use the "Comment" command to add a comment to the batch journal
I use the "Remove" command to remove completed batches from the batch list
I usually only use these when something goes wrong

---
Operations - Recipe Procedure
Operations - Recipe Procedure
This shows the active steps and the transitions being evaluated
I can also use this display to control the recipe procedure
- Another Active-X control is the procedure view
- This can also be included in any HMI display to display and control a specific batch's recipe
I usually only control the order of execution when something goes wrong

---
Recipe Procedure - Control
Recipe Procedure - Control
Performing these actions require I have the right security privileges
- Right click to bring up the menu to control the recipe procedure
- These can also be easily configured as buttons
- The newest version of OpenBatch further integrates these controls into your HMI
  or DCS displays
Security Control is integrated with standard Windows-NT security

---
Operations - Prompts
Operations - Prompts
- When Procedure Manager is not installed, then the "Prompt List" Active-X control provides access to "prompts"
- Prompts are requests for values from the operator
  - These are report parameters that the operator must supply for the batch to continue
I need to enter a value for the batch to continue
Prompts are defined in the recipe editor

---
Classical Operations View
Classical Operations View
- OpenBatch also has a stand alone operations interface
- All of the previous functions, as well as additional functions for debugging, are provided by this Windows-NT application
I can do all batch actions from this application
Usually I will control the batches using the Active-X controls and my HMI or browser

---
Batch Journals and Reports
Batch Journals and Reports
- OpenBatch also collects all of the information about the execution of a batch into a batch log
- Reports can be built against the batch
  log, or the information can go
  into a database for analysis
This information is very valuable, and it is automatically recorded.
The electronic batch log means I need to do less paperwork !

---
OpenBatch Programs
OpenBatch Programs
- The following programs are provided with OpenBatch
- Not all programs need to be installed on all computers
- OpenBatch runs as a full client server architecture
  - Editing may be done from any computer on the network
  - Viewing may be done from any computer network
This starts the equipment editor
This lets me control the batch server
This lets me simulate the control hardware for testing
This starts the standalone OpenBatch viewer
The Archiver saves the batch log into a database
This starts the recipe editor
This starts the report editor

---
Operations Summary
Operations Summary
OpenBatch is the open solution. They work with all major control vendors.
- OpenBatch is recipe execution, batch logging, batch reporting, and recipe editing
- Sequencia provides complete solutions for batch automation
  - OpenBatch
    - Recipe execution
  - Production Manager
    - Manual and semi-automated operations
  - Procedure Manager
    - Integration with ERP systems
OpenBatch works with Honeywell, Rockwell, GE, Aspen Technologies, Siemens, Ci Technologies, and many others.

---
Services and Training
Services and Training
Least we forget, Sequencia also offers services
  - Help in defining the equipment layout and organization
  - Help in defining the phases
  - Help in initial recipe building
- And Training
  - On site
  - Any Sequencia office
Sequencia has a large staff of batch experts to help.
Sequencia wants to make every batch project a successful project !

---
For more information visit our web site at
www.sequencia.com
or contact our sales coordinator at
sales@sequencia.com or call 602-896-3800