A Flow Stream Approach
for
Process Cell Modularization
François Lebourgeois (Rhône Poulenc)
Jean-Michel Rayon (Consultant)
Jean Vieille (Consultant)
World Batch Forum 2000
Brussels, October 2000

---
Summary
- Origin of ASTRID
- Product Processing vs Equipment Control : no longer mixed-up
- Safe Operation vs Flexibility: reducing the risk
- Material & Energy Flow Analysis
- Bottom-up Engineering
- The 4 ASTRID objects
- ASTRID vs S88: how do they fit together?
- Successes and Issues
- Future

---
Origin of ASTRID
- The Story begins in 1988
- WG led by Health, Safety and Environment Management of Rhône-Poulenc
- Part of « Process Control Safety » program
- Focused on Safe Operation of Multipurpose process cell
Operator
Actuators
Control System
Safety Interlock System

---
Product Processing vs Equipment Control: no longer mixed-up
Describe Recipe Procedure
Product Processing Definition
Using Equipment Procedural Elements
EPEs
Granularity against
Flexibility / Complexity
Equipment Control Definition
Define Equipment Procedural Elements
Assemble Process Elements in paths
Detail Process Cell Elements

---
Safe Operation and Flexibility :
Reducing the risk
V1 ?
Reactor #1
Allocated to batch A
Reactor #2
Allocated to batch B

---
Material and Energy Flow analysis
Energy Sources
Energy Sinks
Material Sources
Material Sinks
A
D
B
E
F
C

---
1. Identify Containers
Material Sources
Material Sinks
A
D
B
E
F
C

---
2. Identify realistic Paths
Material Sources
Material Sinks
A
D
B
E
F
C

---
3. Create / check Recipes: Sequence Paths
1
Material Sources
Material Sinks
A
D
B
E
F
C
5
4
3
3
2

---
Bottom-Up Engineering
Identify, highlight & name Containers or RESOURCES on P&ID
  - Analytic Process Equipment check
  - Straightforward, rule-based Process
Identify, highlight & name Paths or FUNCTIONS: Build all elementary flows/paths
  - Combine and attach resources to the path
  - Check ability to execute Recipes
1. Attach DEVICES to Resources
2. Describe FUNCTIONS and RESOURCES behavior

---
Work on P&ID
A
A
A
A
P1

---
Highlight Resources
R1
A
B
R4
R3
R2
C
D
R5
R6
P1

---
Define paths : get functions
F2
R1
F1
A
B
R4
R3
R2
C
D
R5
R6
F3
F1 : Fill A (R1, R2)
F2 : Fill B (R1, R3)
F3 : Transfer B -> C (R3, R4, R5)
…
P1

---
Attach Devices to Resources : manage interlocks
R1
F2
F1
V1
V2
F3
A
B
R4
R3
R2
F3
F3
V5
V6
F3
F3
V3
V4
F3
F3
C
D
R5
R6
F3
Transfer from B to C: F3 is active, F1 and F2 are inactive:
V4 and V5 are controlled by F3
V2,3,6 are locked; F2 is inhibited, F1 is available for use
P1

---
Other applications
The Flow Stream analysis opens interesting domains of application:
  - Sanitary / cross contamination control
  - Capacity limitation
Resource 1
Product X
Dirty
Clean
Resource 2
Product Y
Dirty
Clean
Resource 1
Maximum Capacity
Committed Capacity
Resource 2,3, 4, 5
Required Capacity

---
The 4 ASTRID Objects
R1:
Recipe
F1:
Fill A
F2:
Fill B
F3:
Transfer B-> C
R1:
Feeding Line
R2:
Tank A
R3:
Tank B
R4:
Transfer Line
R5:
Tank C
R6:
Tank D
V1
V2
V3
V4
V5
V6

---
ASTRID vs S88:
How do they fit together
Procedural model
(Functionality)
Procedural model
(Functionality)
Equipment model
Equipment model
PROCEDURE
PROCESS
CELL
FUNCTION
(Path)
FUNCTION
(Behavior,
Chaining,
Sequencing)
UNIT
PROCEDURE
UNIT
OPERATION
PHASE
EQUIPMENT
MODULE
CONTROL
MODULE
RESOURCE
CONTROL
MODULE
DEVICE
S88
ASTRID

---
Successes & Issues
Successes
  - Used for over 10 years
  - 20 plants, 40 Process Cells, 100 Controllers, 40000 I/O ’s
  - New Users since Rhône-Poulenc affiliation (AVENTIS, RODHIA, PASTEUR-MERIEUX):
    - PFITZER, DANONE (LU, KRONENBOURG), SANOFI, (Chemical, F&B, Pharma)
  - Users are fans!
Issues
  - Slow spread: education and promotion needed (as S88)
  - Control System implementation : ASTRID resources availability, programming features

---
Conclusion
ASTRID as an S88 companion
  - for Equipment control: solidification of concepts
ASTRID fans love:
  - Easy to understand, Equipment based Specifications
  - Dynamic and optimized Resource Allocation / Safe Actuator Interlocks
  - Easy Material transfers
  - Information propagation and summarization
  - Operational Qualification support for validation
  - SO SIMPLE!
Future
  - Improvement of ASTRID vs S88 compliance
  - ASTRID vendor libraries in Control Systems
Extensive documentation available at http://fbforg.homepage.com